## Slide 1: Csc333 Data communication & Networking Credit: 2

## Slide 2
digital and analog transmission
asynchronous and synchronous transmission
types of communication services
transmission media
Multiplexing
Noise

## Slide 3: Computer Networks
Concept of computer Networks
network Architecture
types of networks
network topology

## Slide 4
network components
internet and e-mail and its uses in modern communication
satellite communication
Some practical (optional)

## Slide 5: Data Communication
The fundamental purpose of a communications system is the exchange of data between two parties.
Examples include;
A communication between a terminal and a server over a public telephone network,
the exchange of voice signals between two telephones over the same network.

## Slide 6: Basic Elements of Comm. Sys
The key elements of comm. Model are as follows;
Source: This device generates the data to be transmitted; examples are telephones and computers
Transmitter: transforms and encodes the information in such a way as to produce electromagnetic , electrical or light signals that can be transmitted across some sort of transmission system
Transmission system: This can be a single transmission line or a complex network connecting source and destination

## Slide 7
Receiver: The receiver accepts the signal from the transmission system and converts it into a form that can be handled by the destination device
Destination: Takes the coming data from the receiver

## Slide 8
In data communication four basic terms are frequently used. They are:
Data : A collection of facts in raw forms that become information after processing.
Signals : Electric or electromagnetic encoding of data.
Signaling : Propagation of signals across a communication medium.
Transmission : refers to the transfer of data across the network.

## Slide 9
Over a network, data packets use different methods such as unicast, broadcast, and multicast.

## Slide 10: Communication Protocols
Computers send and receive data across a communication links through comm.softwares
The data communication software instructs computer systems and devices as to how exactly data is to be transferred from one place to another
The procedure of data transformation in the form of software is commonly known as protocol

## Slide 11
Protocols perform the following functions for the efficient and error free transmission of data;
Data sequencing
Data Routing
Flow control
Error Control
Examples of communication protocols include;

## Slide 12
TCP : main protocol in TCP/IP networks
TCP uses acknowledgement (ACK) packets and sequence numbers to create a full duplex reliable stream connection between two end points
The connection between client and server begins with a three-way handshake
Client sends a synchronization (SYN) packet to the server with initial sequence number X.

## Slide 13
Server responds by sending a SYN/ACK packet that contains the server’s own sequence number p and an ACK number for the client’s original SYN packet
This ACK number indicates the next sequence number the server expects from the client.
Client acknowledges receipt of the SYN/ACK packet by sending back to the server an ACK packet with the next sequence number it expects from the server, which in this case p+1.

## Slide 14
The next protocol is UDP
It as “a connectionless protocol that, like TCP, runs on top of IP networks
UDP doesn’t use sequence numbers like TCP
HTTP is another protocol
It is “the underlying protocol used by the World Wide Web
HTTP defines how messages are formatted and transmitted
Also define what actions Web servers and browsers should take in response to various commands.

## Slide 15: Data Transmission Modes
There are three ways for transmitting data from one point to another;
Simplex
Half-duplex
Full-duplex

## Slide 16: Digital and Analog Transmission
Data is transmitted from one point to another point by means of electrical signals that may be in digital and analog form.
In analog signal the transmission power varies over a continuous range with respect to sound, light and radio waves
. Analog signal is measured in Volts and its frequency is in Hertz (Hz).

## Slide 17
digital signal may assume only discrete set of values within a given range
It is a sequence of voltage represented in binary form
When digital data are to be sent over an analog form the digital signal must be converted to analog by means of digital to analog converter (DAC).
So the technique by which a digital signal is converted to analog form is known as modulation

## Slide 18
the conversion of analog signal to its digital form, is known as demodulation

## Slide 19: Asynchronous and Synchronous Transmission
Data transmission through a medium can be either asynchronous or synchronous
In asynchronous transmission data is transmitted character by character as you go on typing on a keyboard
Hence there are irregular gaps between characters
it is cheaper to implement, as you do not have to save the data before sending

## Slide 20
in the synchronous mode, the saved data is transmitted block by block
Synchronous transmission is well suited for remote communication between a computer and related devices like card reader and printers

## Slide 21: Types of Communication Services
A term used to describe the data-handling capacity of a communication service is bandwidth.
Bandwidth is the range of frequencies that is available for the transmission of data
The communication data transfer rate is measured in a unit called baud
Baud is identical to bits per second

## Slide 22
Communication companies provide three general classes of service for both voice and data communication
. Narrowband handles low data volumes. Data transmission rates are from 45 to 300 baud
Voiceband handles moderate data transmission volumes between 300 and 9600 baud
Broadband handles very large volumes of data. These systems provide data transmission rates of 1 million baud or more

## Slide 23: Bit Rate and Bandwidth
Bit rate is the number of bits that can be transmitted per second over a channel. It is measured in bits/s
It is the direct measure of information-carrying capacity of a communications link or network for digital transmission
Bandwidth is the frequency range within which a signal can be transmitted without significant deterioration
It is measured in Hertz

## Slide 24
It is the information-carrying characteristic of a communications channel used for analog transmission