TO:		XXXXX, Urban Planer II					Land Development Coordination

FROM:	XXXXXXX, Police Officer

Crime Prevention Unit

DATE:		August 23, 2004

SUBJECT:	File # Z04-133

Attached is the site plan review and CPTED recommendations for File # Z04-133

The site is located in Tampa Police Grid #29 but borders with grid # 30.  It is important to understand crime trends in the area around the proposed site to determine security needs and potential risks.  Crime analysis has been conducted on both grids and no significant trends were observed with the exception being a steady increase in auto burglary occurring in grid #29

Based upon the submitted rezoning petition, the Tampa Police Department will not oppose the rezoning; however, there are several safety issues that need to be addressed.

- Lighting will be metal halide lighting in the form of wall packs mounted on the east and south side of the building if this area is to be used for parking.  IES recommended illumination will be at 6 foot candles at a ratio of 4:1. If parking is not allowed then recommended illumination will be at 3 foot candles at a 4:1 ratio using wall packs.

- Pedestrian scale lighting should be used along N. 13th St..  Lighting should be fluorescent and the fixture should be properly mounted to limit vandalism. IES recommends 3 foot-candles for lighting along sidewalks with a uniformity of 4:1. All lighting will be designed to limit glare and light trespass.

- All landscaping should follow the two foot six foot rule.  All landscaping should be ground cover, two feet or less and lower tree canopies should be at six feet. This increases natural surveillance and eliminates hiding areas with in the landscaping. Tree canopies should not interfere with or block the lighting along sidewalks. This creates shadows and areas of concealment.

- CPTED fencing should be used to separate the activity between the adjoining properties and the site itself. CPTED fencing is fencing that allows for natural surveillance. Wrought iron or decorative fencing is sometimes referred to as CPTED fencing.

- Natural surveillance is an important factor when implementing CPTED. Windows should be uncluttered with no advertising to allow for natural surveillance of the interior. This is especially important along the pedestrian walkway.

Art Hushen, Police Officer

City of Tampa Police Department

| RATING | DESCRIPTION |
| --- | --- |
| HIGH | Double & above the number of crimes in Tampa (>200% +) |
| ABOVE | One & one-half to almost double the number of crimes in Tampa (150% to 199.99%) |
| AVERAGE | Three quarters to almost one & one-half the number of crimes in Tampa (75% to 149.99%) |
| BELOW | One half to almost three quarters the number of crimes in Tampa (50% to 74.99%) |
| LOW | Less than half the number of crimes in Tampa (<less than 50%) |

In evaluating the Part I and Part II crimes that occur most frequently, the Tampa Police Department evaluated the following crimes categories for the years 2001- 2003 for grid #29:

| Grid #29 city-wide comparison for 2001-2003 |
| --- |
| PART I CRIMES |
| Category | Occurrence | Rating | City Average |
| Sexual Assault | 10 | High | 4.40 |
| Robbery | 50 | Above | 30.30 |
| Aggravated Assault | 93 | High | 44.52 |
| Burglary | 244 | High | 88.16 |
| Larceny / Building | 55 | Above | 38.31 |
| Burglary of Vehicle | 238 | Above | 144.47 |
| Vehicle Theft | 134 | Average | 93.24 |
| PART II CRIMES |
| Vandalism | 78 | High | 49.38 |
| Prostitution | 23 | High | 10.12 |
| Liquor Law Violations | 10 | Below | 18.05 |
| Simple Assault | 173 | High | 83.10 |
| Drugs | 92 | Average | 64.25 |

| RATING | DESCRIPTION |
| --- | --- |
| HIGH | Double & above the number of crimes in Tampa (>200% +) |
| ABOVE | One & one-half to almost double the number of crimes in Tampa (150% to 199.99%) |
| AVERAGE | Three quarters to almost one & one-half the number of crimes in Tampa (75% to 149.99%) |
| BELOW | One half to almost three quarters the number of crimes in Tampa (50% to 74.99%) |
| LOW | Less than half the number of crimes in Tampa (<less than 50%) |

In evaluating the Part I and Part II crimes that occur most frequently, the Tampa Police Department evaluated the following crimes categories for the years 2001- 2003 for grid #38:

| Grid #38 city-wide comparison for 2001-2003 |
| --- |
| PART I CRIMES |
| Category | Occurrence | Rating | City Average |
| Sexual Assault | 7 | Above | 4.40 |
| Robbery | 72 | High | 30.30 |
| Aggravated Assault | 127 | High | 44.52 |
| Burglary | 230 | High | 88.16 |
| Larceny / Building | 34 | Average | 38.31 |
| Burglary of Vehicle | 194 | Average | 144.47 |
| Vehicle Theft | 128 | Average | 93.24 |
| PART II CRIMES |
| Vandalism | 88 | Above | 49.38 |
| Prostitution | 25 | High | 10.12 |
| Liquor Law Violations | 12 | Below | 18.05 |
| Simple Assault | 174 | High | 83.10 |
| Drugs | 90 | Average | 64.25 |

| GRID 29 |
| --- |
|  | Murder | Sexual Battery | Robbery | Aggravated Assault | Burglary | Theft | Auto Burglary | Motor Vehicle Theft |
| 1999 | 0 | 4 | 17 | 39 | 57 | 58 | 40 | 38 |
| 2000 | 0 | 4 | 11 | 47 | 70 | 34 | 57 | 65 |
| 2001 | 0 | 5 | 18 | 33 | 113 | 53 | 75 | 53 |
| 2002 | 0 | 3 | 18 | 28 | 64 | 45 | 79 | 49 |
| 2003 | 0 | 2 | 13 | 31 | 67 | 28 | 84 | 31 |
| Total | 0 | 18 | 77 | 178 | 371 | 218 | 335 | 236 |

| GRID 38 |
| --- |
|  | Murder | Sexual Battery | Robbery | Aggravated Assault | Burglary | Theft | Auto Burglary | Motor Vehicle Theft |
| 1999 | 0 | 2 | 40 | 55 | 46 | 52 | 24 | 30 |
| 2000 | 0 | 3 | 31 | 52 | 74 | 38 | 39 | 36 |
| 2001 | 1 | 3 | 26 | 55 | 70 | 41 | 56 | 43 |
| 2002 | 0 | 1 | 22 | 37 | 63 | 38 | 65 | 57 |
| 2003 | 0 | 3 | 22 | 34 | 96 | 38 | 73 | 28 |
| Total | 1 | 12 | 141 | 233 | 349 | 207 | 257 | 194 |

| GRID 29 |
| --- |
|  | UCR PART 1 CRIMES | UCR PART 2 CRIMES | TOTAL REPORTED CRIME |
| 1999 | 253 | 199 | 452 |
| 2000 | 288 | 229 | 517 |
| 2001 | 350 | 162 | 512 |
| 2002 2003 | 286 256 | 203 183 | 489 439 |
| total | 1,433 | 976 | 2,409 |

| GRID 38 |
| --- |
|  | UCR PART 1 CRIMES | UCR PART 2 CRIMES | TOTAL REPORTED CRIME |
| 1999 | 249 | 276 | 525 |
| 2000 | 273 | 251 | 524 |
| 2001 | 295 | 188 | 483 |
| 2002 2003 | 283 294 | 156 181 | 439 475 |
| total | 1,394 | 1,052 | 2,446 |